## Slide 1
Notebook + verified run HMC-N1N2-20261007
01 / 12
MID-VIVA • PROJECT PROGRESS
EEG Sleep Classification and
Reference-Based Sleep-Health Profiling
Biomarker-assisted N1/N2 refinement
Rikin Parekh · Om Ahuja
23BIT044 · 23BIT014
Guide: Dr. Santosh Sathpathy
Information and Communication Technology
Pandit Deendayal Energy University
Notes: Opening: Our project classifies five sleep stages, adds a targeted spectral refiner for N1/N2, and derives descriptive recording profiles. This is a progress presentation. The main implementation is the biomarker N1/N2 refinement notebook. Names and institutional details are retained from the existing deck.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 2
Introduction, motivation and objectives
Context: U-Sleep (2021), RobustSleepNet (2021); project notebook
02 / 12
Sleep staging assigns a label to each 30-second EEG segment.
Wake
N1
N2
N3
REM
Motivation
Manual scoring takes time.
N1/N2 discrimination remains
a difficult part of automation.
Research question
Can spectral EEG features
complement the existing
five-stage classifier?
Current objectives
Improve N1/N2 labels.
Generate a hypnogram.
Summarize recording profiles.
Five output classes represent Wake, three NREM stages, and REM sleep.
Notes: EEG measures electrical activity at scalp electrodes; sleep staging turns successive epochs into a hypnogram. The objective is complementary spectral information for N1/N2, rather than an unsupported claim of diagnostic accuracy. The project extends an existing saved classifier. The stage strip lists classes; the arrows represent the label sequence concept, not physiologically mandatory transitions.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.
https://www.nature.com/articles/s41746-021-00440-5
https://arxiv.org/abs/2101.02452

## Slide 3
Literature review and project direction
Selected primary papers; full citations and links in speaker notes
03 / 12
Study | Main contribution | Relevance to our project
DeepSleepNet Supratak et al., 2017 | CNN features + BiLSTM across EEG epochs | Compare a learned sequence-context baseline
SeqSleepNet Phan et al., 2019 | Hierarchical recurrent sequence-to-sequence staging | Add context between epochs; current model is within-epoch
U-Sleep Perslev et al., 2021 | Fully convolutional staging across clinical cohorts | Test transfer and robustness on a separate dataset
RobustSleepNet Guillot & Thorey, 2021 | Montage flexibility and leave-one-dataset-out testing | Check channel compatibility and external generalization
SLEEPYLAND Dei Rossi et al., 2025* | Standardized evaluation; SOMNUS soft-voting ensemble | Test model fusion and calibrate the final output
Design direction: targeted experts + sequence context + fair external evaluation
*2025 arXiv preprint. Published scores use different datasets and protocols; no direct ranking is claimed.
Notes: Literature review: DeepSleepNet: a Model for Automatic Sleep Stage Scoring based on Raw Single-Channel EEG, Supratak et al., IEEE TNSRE 2017, DOI 10.1109/TNSRE.2017.2721116. SeqSleepNet: End-to-End Hierarchical Recurrent Neural Network for Sequence-to-Sequence Automatic Sleep Staging, Phan et al., IEEE TNSRE 2019, DOI 10.1109/TNSRE.2019.2896659. U-Sleep: resilient high-frequency sleep staging, Perslev et al., npj Digital Medicine 2021, DOI 10.1038/s41746-021-00440-5. RobustSleepNet: Transfer learning for automated sleep staging at scale, Guillot and Thorey, 2021. SLEEPYLAND: trust begins with fair evaluation of automatic sleep staging models, Dei Rossi et al., 2025 arXiv preprint. These papers motivate context, robust evaluation and soft fusion. Our proposed coarse/NREM hierarchy is an engineering hypothesis, not an implementation attributed to any of these papers. Different data, channels and evaluation protocols prevent score comparison.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.
https://arxiv.org/abs/1703.04046
https://arxiv.org/abs/1809.10932
https://arxiv.org/abs/2101.02452
https://www.nature.com/articles/s41746-021-00440-5
https://arxiv.org/abs/2506.08574

## Slide 4
Dataset and 30-second EEG epochs
PhysioNet HMC v1.1; verified split_summary.json
04 / 12
HMC v1.1: 151 clinical PSG recordings; project subset: 24 recordings
Partition | Recordings | EEG epochs
Training | 16 | 15,216
Validation | 4 | 3,619
Test | 4 | 3,109
Total | 24 | 21,944
One EEG epoch = one 30 s segment
0–30 s
30–60 s
60–90 s
At 100 Hz: 30 × 100 = 3,000 samples
Four channels → input shape 4 × 3,000
F4-M1 · C4-M1 · O2-M1 · C3-M2
Split by recording ID. SN001 covers only 190 epochs (95 min); whole-night claims are unsupported.
Notes: PSG means polysomnography. HMC is a heterogeneous clinical population, not a healthy normative database. Four EEG derivations and original 256 Hz sampling are documented. We use a 24-recording subset, separated by recording ID into 16/4/4. IDs identify recordings; a repeated-person mapping is not provided, so person-level separation is not proven. Test IDs: SN001, SN004, SN009, SN022. EEG epoch is a temporal segment, whereas training epoch means one pass through the training data. Stored SN001 is a 95-minute segment. Dataset total is 15,216+3,619+3,109=21,944.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.
https://physionet.org/content/hmc-sleep-staging/1.1/

## Slide 5
EEG preprocessing
Notebook preprocessing lineage; archived matched SN009 signal example
05 / 12
Select 4
channels
50 Hz notch
at 256 Hz
Bandpass
0.3–35 Hz
Resample
to 100 Hz
30 s epochs
+ normalize
Raw EEG · SN009, F4-M1
Filtered and normalized EEG · same interval
Per-epoch, per-channel normalization. Apply the 50 Hz notch before resampling.
Archived 300–330 s signal illustration only; all performance results use the current 3,109-epoch run.
Notes: Source pipeline order from preprocessing_config.json: selected four channels, notch 50 Hz at original sampling rate, bandpass 0.3–35 Hz, resample 100 Hz, epoch and channel normalization. The current refinement notebook loads stored preprocessed NPZ EEG and normalizes each epoch again for neural inference; spectral extraction uses stored EEG before that second normalization. Automatic artifact rejection was not established in the source preprocessing; explicit quality gates are future work. Existing example metadata: SN009, F4-M1, index 10, 300–330 seconds, raw 256 Hz, processed 100 Hz; saved/reprocessed difference 0.0. These figures are retained as explanatory signal evidence from ppt_artifacts, not as evidence for the current numerical comparison.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 6
Implemented system block diagram
Notebook + verified run HMC-N1N2-20261007
06 / 12
Main implementation: Biomarker_N1_N2_Refinement.ipynb
Stored EEG
4 × 3,000
Fast SCFormer-U
5-stage output
Predicted N1/N2?
Spectral refiner
Final stage
per epoch
Welch spectral
features
Mean EEG features
per recording
Hypnogram +
sleep architecture
Recording profile
+ reference comparison
Architecture + spectral features → z-scores / P10–P90 → four-domain profile → dashboard
The 16-recording training reference provides dataset-relative descriptions.
Notes: Read the top path left to right: stored input, retained five-stage model, targeted N1/N2 refinement, final labels. Welch features support the refiner (shown explicitly on slide 8) and recording EEG means. Final labels produce architecture metrics. Both architecture and spectral means join the recording profile; the lower connector carries architecture into that profile. Ten architecture metrics determine four domain flags; EEG deviations are displayed separately. The training reference uses only 16 training recordings. The resulting profile is descriptive, not a diagnosis.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 7
Existing model and training epochs
Notebook + verified run HMC-N1N2-20261007
07 / 12
Conv1D encoder
64 → 128 filters
Self-attention
4 heads, key dim 16
BiLSTM
64 units / direction
Pooling + dense
5 evidence outputs
226,309 parameters · Attention and BiLSTM operate within each 30-second EEG epoch
Training / validation accuracy
Chart: Training epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Training | 0.44263 | 0.60331 | 0.67146 | 0.69946 | 0.71648 | 0.73528 | 0.74474 | 0.74993 | 0.7594 | 0.76617
Validation | 0.16524 | 0.17684 | 0.23902 | 0.41393 | 0.60901 | 0.64465 | 0.62669 | 0.64438 | 0.67975 | 0.65239
A training epoch = one full
pass through training data
Adam · learning rate 0.0001
Batch size: 128
10 training epochs
Selected checkpoint: epoch 9
Current notebook loads this checkpoint; it trains the spectral refiner separately.
Notes: Architecture verified against model_layers.csv and saved checkpoint: first convolution kernel 7/stride 4, second kernel 5/stride 4, 64 and 128 filters; 4-head attention with key dimension 16, residual normalization/feed-forward layers; within-epoch bidirectional LSTM, 64 units in each direction; pooling, dense and five softplus evidence outputs. 226,309 total parameters. Dirichlet alpha=evidence+1; probability alpha/sum(alpha); original uncertainty=5/sum(alpha). Training chart is the saved historical training log for this retained model, not a new run. Ten maximum and actual training epochs, checkpoint selected at 9 by validation evidential accuracy (67.97%). No automatic scheduler in final training cell. The biomarker notebook loads the checkpoint and fits the refiner without retraining this neural model.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 8
N1/N2 refinement flowchart
Notebook + verified run HMC-N1N2-20261007
08 / 12
Initial stage
prediction
N1 or N2?
YES
9 spectral features
+ StandardScaler
Balanced logistic
regression → N1 / N2
NO
Retain original Wake / N3 / REM prediction
Feature group | Input to the refiner
Relative powers | Delta, Theta, Alpha, Sigma, Beta
Band / Delta ratios | Theta, Alpha, Sigma, Beta
Fit on training data only
True AND predicted N1/N2:
1,278 N1 + 4,588 N2 epochs
Test gate uses predictions only.
Welch: 4 s windows, 2 s overlap; average channel powers before computing ratios.
Notes: Exact training gate from notebook cells 20–21: true labels AND baseline predictions in {N1,N2}. This produces 5,866 training candidates. Pipeline: StandardScaler then LogisticRegression(class_weight="balanced", max_iter=2000, random_state=42). At inference, ONLY the initial predicted label routes the epoch. Ground truth is never an inference input. Nine features: relative Delta/Theta/Alpha/Sigma/Beta plus Sigma/Delta, Theta/Delta, Alpha/Delta, Beta/Delta. Bands: [0.5,4), [4,8), [8,12), [12,16), [16,30) Hz. Welch at 100 Hz uses 400 samples/window and 200 overlap; total power [0.5,30). Four channel powers are averaged first. Sigma power does not measure spindle density. Original predicted Wake/N3/REM labels are kept; original neural probabilities and uncertainty are not recalibrated to the refined labels.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 9
Results and measured gains
Notebook + verified run HMC-N1N2-20261007
09 / 12
Chart: 
| Accuracy | Macro F1 | N1 F1 | N2 F1
Existing model | 0.55452 | 0.57416 | 0.36604 | 0.57117
N1/N2 refined | 0.59344 | 0.59512 | 0.40632 | 0.63572
+3.89 pp
Accuracy: 55.45% → 59.34%
+2.10 pp
Macro F1:
57.42% → 59.51%
154 corrected − 33 degraded = 121 net additional correct epochs
Same 3,109 test epochs across 4 recordings · 238 labels changed · pp = percentage points
Notes: Current experiment HMC-N1N2-20261007 only. Raw/refined accuracy: 0.5545191379864909 / 0.5934384046317144; macro F1 0.5741553020766511 / 0.5951219684303188. N1 F1 0.3660403618649965 / 0.4063241106719368; N2 F1 0.571173583221776 / 0.6357231661831745. Accuracy gain 3.8919267 percentage points; macro F1 gain 2.0966666 percentage points, rounded once to 3.89/2.10. Corrections 154, degradations 33, wrong-to-wrong 51, unchanged 2,871, total 3,109. Of 238 changes, 121 are net additional correct. N2-to-N1 errors 506 to 379. N1 F1 gain 4.03 pp; N2 F1 gain 6.45 pp. Kappa 0.4253 to 0.4647. Per-stage Wake/N3/REM F1 remain unchanged because predictions of these stages are retained. Results are modest and limited to this small subset; not a comparison against the literature datasets.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 10
Project outputs: hypnogram and sleep profile
Notebook + verified run HMC-N1N2-20261007
10 / 12
SN009 · verified stage sequence
Sleep Studio · current GUI
Architecture, spectral features,
reference deviations and exports
Stage labels → architecture metrics → training-reference comparison → four-domain profile
Duration · Continuity · Initiation · Architecture | Descriptive research profiles, not diagnoses
Notes: Hypnogram is the verified SN009 plot showing original and refined labels versus ground truth. SN009 has 901 epochs. Dashboard screenshot is from the current verified GUI; it demonstrates implemented outputs rather than a mockup. Master features have recording ID + 22 numeric fields; compare 21 fields after excluding recording_minutes. Architecture metrics include TST, efficiency, SOL, WASO, stage percentages, awakenings and project-defined fragmentation. Efficiency uses evaluated duration; stage percentages use TST. Reference mean/sample SD and P10/P90 derive from 16 training recordings; any out-of-interval architecture metric flags the corresponding domain. Four domains are Duration, Continuity, Initiation, Architecture. SN009: one deviated domain, descriptive Mild Deviation. EEG deviations do not contribute additional domains. HMC is clinical, not healthy normative data; in-sample architecture reference and unknown whole-night timing limit interpretation. Current GUI has PDF/JSON/CSV/ZIP exports and a Colab worker; live SN009 predictions were already independently reproduced.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.

## Slide 11
Future plan: multistage, multimodel architecture
Proposed research design; inspired by SeqSleepNet, RobustSleepNet and SLEEPYLAND
11 / 12
Proposed • not yet implemented or evaluated
Aligned EEG
+ quality checks
Model A: coarse CNN
Wake / REM / NREM
Model B: NREM expert
N1 / N2 / N3
Soft probability
composition +
optional baseline fusion
Model C: TCN
Temporal CNN
across epochs
Conditional NREM probabilities preserve five-class normalization
1 Experts
Test coarse + NREM models
against the current baseline.
2 Context + confidence
Train TCN on out-of-fold outputs.
Calibrate final probabilities.
3 Broader validation
New locked cohort, then external
data and optional EOG / EMG.
Notes: Proposed engineering design, not current implementation. Train compact Model A with Wake/REM/NREM targets, Model B on true training NREM epochs. Evaluate B on each inference epoch. Let g be coarse probabilities and h be conditional NREM probabilities: q=[gW,gNREM*hN1,gNREM*hN2,gNREM*hN3,gREM]. This sums to 1. Optional soft fusion r=lambda*q+(1-lambda)*p with the retained five-stage model p; choose lambda on development data only. Avoid hard gating because coarse mistakes could otherwise become irreversible. Model C is a small temporal convolutional network operating across consecutive epochs, unlike current within-epoch BiLSTM. Train it on out-of-fold expert predictions, preserve recording boundaries/gaps, then calibrate final output on a held-out validation partition. TCN and Viterbi are alternatives to compare by ablation, not refiners to stack automatically. Add EOG/EMG specialists only if aligned data and missing-modality tests are available. Start small with 24 recordings to limit overfitting. Current four test recordings have already been examined; reserve genuinely new recordings/person cohort before new tuning. Person-level grouping requires a verified mapping. Sequence context motivated by SeqSleepNet and L-SeqSleepNet; heterogeneous cohort testing by RobustSleepNet; soft voting and fair evaluation by SLEEPYLAND. Benefits are hypotheses, not guaranteed gains.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.
https://arxiv.org/abs/1809.10932
https://arxiv.org/abs/2301.03441
https://arxiv.org/abs/2101.02452
https://arxiv.org/abs/2506.08574

## Slide 12
Conclusion and next milestones
Notebook + verified run HMC-N1N2-20261007
12 / 12
What is demonstrated
Spectral features improve
N1/N2 discrimination
in the current experiment.
59.34% test accuracy; 59.51% macro F1.
A complete notebook-to-GUI pipeline
produces stage labels and profiles.
Limits: 4 test recordings, partial SN001,
N1 F1 40.63%, no clinical validation.
Next milestones
01 Audit full EDF alignment and quality;
reserve a new locked test cohort.
02 Compare experts, soft fusion and TCN
through controlled ablations.
03 Evaluate calibration, external data
and biomarker errors; add modalities.
Evaluate macro F1, N1/N2 F1, calibration,
latency and errors in sleep biomarkers.
Notes: Conclusion: the current reproducible experiment supports complementary spectral features for N1/N2. Net correction is 121 epochs and the gains are modest. The project also implements recording architecture and spectral features, descriptive reference profiles, a Windows Electron GUI and reports. It does not establish clinical diagnosis or superior performance versus the literature. Roadmap: verify original EDF alignment, retain timestamp continuity and quality checks, expand HMC data and reserve untouched recordings/person cohort; compare flat baseline, coarse/NREM composition, optional soft fusion, temporal model, and decoder alternatives on identical locked epochs. Fit scalers, class weights and transitions on training data only; use grouped development folds and out-of-fold base predictions for stacking. Report accuracy, macro F1, per-stage F1, kappa, ECE, error-detection AUROC, risk-coverage, latency and model size. Include recording/person bootstrap confidence intervals, stage distribution and individual recording variability. Validate TST/WASO/SOL/stage fractions against label-derived ground truth using verified denominators. Test external dataset/channel compatibility and optional aligned EOG/EMG specialists. No accuracy target or delivery date is promised without experiments.
Project evidence: Biomarker_N1_N2_Refinement.ipynb; refinement_artifacts/verified; independent reproduction HMC-N1N2-20261007.
https://physionet.org/content/hmc-sleep-staging/1.1/
https://arxiv.org/abs/2101.02452
https://arxiv.org/abs/2506.08574